## Slide 1: Qt5 on TI processors

## Slide 2: Qt5 differences with Qt4
With the platform plugin approach - the HW "platform" is expected to provide OpenGL ES2, and any other additional HW acceleration on top of that as part of the platform. In essence - with GLES2 - every screen update in Qt5 happens via an OpenGL ES texturing operation, rather than any other means. In addition to this fundamental change, Qt5 brings in another major programming model update - that of QML, Qt3D etc.
A key thing specific to our (SGX based) platforms - With the elimination of the display plugin, Qt5 no longer uses or supports blits via pvr2d or wsegl, and instead directly uses the egl (or window) capabilities exposed by the GL driver. This eliminates immediately a large portion of pvr2d/wsegl version related issues that cropped up in earlier Qt versions. (ex patch for Qt4 in below link is not needed anymore) https://github.com/prabindh/qt-configs/blob/master/qt4.8/001_wsegl2.patch

## Slide 3: Qt5 platform plugins
The below platform plugins are available in the Qt5 Alpha package. Only "eglfs" and "minimal" are built by default in qtbase.
  cocoa eglfs linuxfb minimal openvglite pro qvfb windows directfb kms openkode openwfd qnx xcb

## Slide 4: Pre-requisites for Qt5 build
- Qt5 alpha source package http://releases.qt-project.org/qt5.0/alpha/
- TI Graphics SDK (4.05 or later) http://software-dl.ti.com/dsps/dsps_public_sw/sdo_sb/targetcontent/gfxsd... http://processors.wiki.ti.com/index.php/AM35x-OMAP35x_Graphics_SDK_Getti... - Recent filesystem (GCC 4.5 or later) - ARM cross Toolchain (GCC 4.5 or later), example from below: http://people.linaro.org/~michaelh/incoming/binaries/

## Slide 5: Configuring Qt5 - eglfs
- a linaro toolchain (linux-arm-gnueabi-) - sgxconfiguro is used (package config for TI Graphics SDK - egl and x11) https://github.com/prabindh/sgxconfiguro - force-pkg-config is used
If this does not seem clear, the older tried-and-tested-method of specifying all possible (and needed) paths in the qmake.conf as below will also work :
https://github.com/prabindh/qt-configs/tree/master/qt5.0_mar2012
The below method adopts the first approach and uses the standard Qt5 supplied linux-arm-gnueabi-g++ mkspec without change
$cd qtbase $export PATH=/opt/linaro/gcc-linaro-arm-linux-gnueabi-2012.03-20120326_linux/bin:/home/prabindh/work1/arm-qt5-tar/qt-everywhere-opensource-src-5.0.0/qtbase/bin: $export PKG_CONFIG=./x86-cross-ubuntu-pkg-config $./configure -prefix /home1/prabu/qt5_install -release -make libs -xplatform linux-arm-gnueabi-g++ -opengl es2 -confirm-license -opensource -no-xcb -no-wayland -force-pkg-config -make examples -make demos -verbose

## Slide 6: Sample config log
Debug .................. no QtDBus module .......... no QtConcurrent code ...... yes QtGui module ........... yes QtWidgets module ....... yes JavaScriptCore JIT ..... To be decided by JavaScriptCore Declarative debugging ...yes STL support ............ yes PCH support ............ yes iWMMXt support ......... no NEON support ........... yes IPv6 ifname support .... yes getaddrinfo support .... yes getifaddrs support ..... yes Accessibility .......... yes NIS support ............ yes CUPS support ........... no Iconv support .......... yes Glib support ........... yes GStreamer support ...... no PulseAudio support ..... no Large File support ..... yes GIF support ............ plugin JPEG support ........... plugin (qt) PNG support ............ yes (qt) zlib support ........... yes Session management ..... auto libudev support ........ no OpenGL support ......... yes (OpenGL ES 2.x) OpenVG support ......... no XShape support ......... auto XVideo support ......... auto XSync support .......... auto Xinerama support ....... runtime Xcursor support ........ runtime Xfixes support ......... runtime Xrandr support ......... runtime Xi support ............. runtime MIT-SHM support ........ auto FontConfig support ..... auto XKB Support ............ auto immodule support ....... yes GTK theme support ...... auto SQLite support ......... plugin (qt) OpenSSL support ........ no Alsa support ........... no libICU support ......... no PCRE support ........... qt Xcb support ............ no Xrender support ........ no EGLFS support .......... yes

## Slide 7: Beyond qtbase
After configure, make && make install are to be done. This is important, as qmake needs to be in the install path.
Steps to build Qt3D :
To build Qt3D, in addition to qtbase also need to build the below:
qtjsbackend (has v8) qtdeclarative qt3d
To build the above, enter the directory, then perform (assuming qmake is in the path as specified earlier) $ qmake && make && make install

## Slide 8: Executing demos on target
After installing the above build on to target, there are several changes from the point of view of Qt4 users, for getting the demos to work.
1) Configure resolution of the screen for Qt
If screen resolution is 16 bpp (RGB565) export QT_QPA_EGLFS_DEPTH=16
edit: If screen resolution is 24 bpp (RGB888) export QT_QPA_EGLFS_DEPTH=24
If this step is not performed, any application running on eglfs platform will abort, with a message as below:
"Initialized display 1 4 Cant find EGLConfig, returning null config Could not create the egl surface: error = 0x3005" Abort

## Slide 9: Running the Demos with eglfs
2) Ensure SGX drivers are installed, and standard GLES2 3D demos are functional without Qt
3) There is no need anymore to set /etc/powervr.ini to QWS library (no such library exists in Qt5) making it simpler to run. Qt5 works with both FRONT and FLIP modes (as of Qt5 Alpha) with "eglfs".
4) Running QML demos:
QMLScene can be used to run QML demos, with a command similar to below: /bin/qmlscene examples/qtdeclarative/qtquick/animation/pathanimation/pathanimation.qml -platform eglfs
5) Running standalone demos:
Standalone qt5 demos (including qt3d demos, as well as classic qtbase demos like animatedtiles) can be invoked as below for eglfs platform plugin
<demo> -platform eglfs

## Slide 10: Qt5 with Xcb
What is Xcb ?
From xcb.freedesktop.org
  The X protocol C-language Binding (XCB) is a replacement for Xlib featuring a small footprint, latency hiding, direct access to the protocol, improved threading support, and extensibility.

## Slide 11: Configuring with Xcb
$cd qtbase $export PATH=/opt/linaro/gcc-linaro-arm-linux-gnueabi-2012.03-20120326_linux/bin:/home/prabindh/work1/arm-qt5-tar/qt-everywhere-opensource-src-5.0.0/qtbase/bin: $export PKG_CONFIG=./x86-cross-ubuntu-pkg-config $./configure -prefix /home1/prabu/qt5_xcb_install -release -make libs -xplatform linux-TIarmv7-sgx-g++ -opengl es2 -confirm-license -opensource -xcb -no-wayland -force-pkg-config -make examples -make demos -verbose

## Slide 12: Configure logs with Xcb
Build .................. libs examples demos Configuration .......... cross_compile release shared dll qpa largefile stl precompile_header neon pcre minimal-config small-config medium-config large-config full-config fontconfig libudev evdev xlib xrender xcb-xlib accessibility egl eglfs opengl opengles2 qpa reduce_exports reduce_relocations clock-gettime clock-monotonic mremap getaddrinfo ipv6ifname getifaddrs inotify png system-freetype system-zlib nis iconv glib xcb alsa icu concurrent audio-backend v8 v8snapshot release Debug .................. no QtDBus module .......... no QtConcurrent code ...... yes QtGui module ........... yes QtWidgets module ....... yes JavaScriptCore JIT ..... To be decided by JavaScriptCore Declarative debugging ...yes STL support ............ yes PCH support ............ yes iWMMXt support ......... no NEON support ........... yes IPv6 ifname support .... yes getaddrinfo support .... yes getifaddrs support ..... yes Accessibility .......... yes NIS support ............ yes CUPS support ........... no Iconv support .......... yes Glib support ........... yes GStreamer support ...... no PulseAudio support ..... no Large File support ..... yes GIF support ............ plugin JPEG support ........... plugin (qt) PNG support ............ yes (qt) zlib support ........... system Session management ..... auto libudev support ........ yes OpenGL support ......... yes (OpenGL ES 2.x) OpenVG support ......... no XShape support ......... auto XVideo support ......... auto XSync support .......... auto Xinerama support ....... runtime Xcursor support ........ runtime Xfixes support ......... runtime Xrandr support ......... runtime Xi support ............. runtime MIT-SHM support ........ auto FontConfig support ..... auto XKB Support ............ auto immodule support ....... yes GTK theme support ...... auto SQLite support ......... plugin (qt) OpenSSL support ........ no Alsa support ........... yes libICU support ......... yes PCRE support ........... qt Xcb support ............ limited (old version) Xrender support ........ yes EGLFS support .......... yes

## Slide 13: Beyond qtbase with Xcb
Refer earlier steps with eglfs, for building the rest of the modules

## Slide 14: Executing demos on target with Xcb
Compared to eglfs approach, since the rendering is handled by Xserver, there is no need to set QPA basics (for ex. resolution).
1) Ensure SGX drivers are installed, and standard GLES2 3D demos are functional without Qt (refer to below link for more details on Xorg build)
http://processors.wiki.ti.com/index.php/Graphics_SDK_Quick_installation_...
2) With the Graphics SDK correctly installed, the /etc/powervr.ini file will have the correct WindowSystem already set. WindowSystem=libpvrPVR2D_DRIWSEGL.so

## Slide 15: Running further Xcb demos
3) Running QML demos:
QMLScene can be used to run QML demos, with a command similar to below: /bin/qmlscene examples/qtdeclarative/qtquick/animation/pathanimation/pathanimation.qml
Note that if the SGX accelerated Xserver is not running on the system, the below message will be printed, and the demo will not run
No platform plugin argument was specified, defaulting to "xcb". QXcbConnection: Could not connect to display Aborted
4) Running standalone demos:
Standalone qt5 demos (including qt3d demos, as well as classic qtbase demos like animatedtiles) can be invoked as below for Xcb platform (default), after entering into the demo folder
./
ex, ./collidingmice
No arguments are necessary as Xcb platform is the default.

## Slide 16: Demo videos/ Binary Qt5 builds for ARM
Available at
http://gpupowered.org/node/10
http://gpupowered.org/node/8
Note – demo videos are captured running on DM3730+SGX GPU platform

## Slide 17: References/ Follow ups
http://gpupowered.org/node/10
http://gpupowered.org/node/8
http://tigraphics.blogspot.com
http://twitter.com/tigraphics_twit